## Slide 1
NAO and Pepper Tutorial
Margot Neggers Raymond Cuijpers m.m.e.neggers@tue.nl r.h.cuijpers@tue.nl
Technische Universiteit Eindhoven Human-Technology Interaction

## Slide 2: Topics
    The NAO Robot
    The Pepper Robot
    Reserving the robots
    Using Choregraphe
    Using Python
    Using NAO lib

## Slide 3: The NAO Robot
    60-cm tall humanoid robot
    Bender Marvin ???

## Slide 4: Working with NAO
    Unbox NAO
    Carry NAO at the waist
    Before switching the robot on: plug in the router
    Chest button
      On (1 press) “OGNAK GNOUK”
      Off (4 seconds) “GNOUK GNOUK”
      When on (1 press) “Hello, I am Marvin. My Internet address is … + Status notifications”
      When on (2 press) Switch on/off autonomous life

## Slide 5: Working with NAO
    While testing
      First test on simulated robot if possible
      Always place the robot on the floor
      Always use soft foam behind the robot
    Charger goes in the back
    Putting the robot back in the box
      It only fits in one way
      If you cannot close the suitcase/lid: move the robot until the lid closes
      Do not push the lid

## Slide 6: The Pepper Robot
    120-cm tall humanoid robot
    Eve

## Slide 7: Working with Pepper
    Preferably only move Pepper when it is turned off
      One hand on the hip and one on the shoulder
      If it is turned on, only move in crouch mode and with power hatch open!
    Chest button
      On (1 press) “OGNAK GNOUK”
      Off (4 seconds) “GNOUK GNOUK”
      When on (1 press) “Hello, I am Eve. My Internet address is … + Status notifications”
      When on (2 press) Switch on/off autonomous life
    Emergency turn off: Red button in neck
      You DO NOT need to OPEN FLAP

## Slide 8: Working with Pepper
    While testing:
      Make sure Pepper has enough space to move around
    Charger goes in the foot, turn the charger right until it clicks
    After turning the robot off, leave it in the lab. It does not have to be put in its box

## Slide 9: NAO Robot and Pepper robot
    Questions/or more details needed?
    http://doc.aldebaran.com/2-4/index.html
    (or check out the help function of choregraphe)

## Slide 10: Reserving the robots
    Send a meeting request to one of the robots:
    Hti.pepper.eve@tue.nl
    Hti.nao.bender@tue.nl
    Hti.nao.marvin@tue.nl
    Include in your meeting request:
    Names of people who will work with the robot
    Location in Atlas
      preferably the social robotics lab (also needs to be reserved)
      Preferable on the 8th or 9th floor
    Reason of reservation (experiment or testing)
    Phone number of one of the students who is using it.

## Slide 11: Using Choregraphe

## Slide 12: Installation
    Install Choregraphe 2.1.4 for NAO and Choregraphe 2.5.10 for Pepper
      https://community.ald.softbankrobotics.com/en/resources/software/language/en-gb
      Create an account
      License is on the same site

## Slide 13: Using Choregraphe
Connect
Autonomous life
Robot view
Behaviors
Drag behaviors
here

## Slide 14: Behaviours

## Slide 15: Example

## Slide 16: Adjust code

## Slide 17: Connecting with the real robot
    Only one Choregraphe at the same time

## Slide 18: Creating animations
    Using animation mode
      Watch the color of the eyes
    Adjusting the joints of the virtual robot

## Slide 19: Timeline
      (1) Upper part timeline with numbered frames. Lower part contains the keyframes
      (2) list of parallel behaviors
      (3) timeline edit button, the current frame indicator, and the general timeline scrollbar.

## Slide 20: Animating the robot
The timeline box is extremely handy to program gestures and movements.
It contains a nice graphical interface for stop-motion animation of the robot
Best of all, the gesture/motion can be exported to python and “run” using the nao.RunMovement() command
Right click here for direct animation
Use Edit button for advanced features

## Slide 21: Directly storing keyframes
  Move the robot into the desired posture manually
    Turn arm/leg/head/body motors off and move limb into position
  Select a frame position on the timeline
  Press (or use context menu of timeline, see below)
    F8 Store Whole body, F9 Store Head
    F10 Store Arms, F11 Store Legs
  Repeat until entire movement is programmed
  Right click on timeline to activate the context menu
    Choose Export Motion to Clipboard/Python/Bezier
  Note: the framerate is normally 25 frames/second, so DO NOT put keyframes to close to each other or you will get very fast movements
  Always test with virtual robot first

## Slide 22: Advanced stop-motion recording
Check manual for details!
Make sure to enable recording buttons
Choose settings for selecting an advanced recording mode
You can select here which joints or joint groups to record

## Slide 23: Editing recorded motions

## Slide 24: Using Python and Naoqi

## Slide 25: Manual Python Installation
    Install the 32-bit version of Python 2.7
    Install the Naoqi SDK for Python (2.1.4 for NAO and 2.5.5 for Pepper)
    Open the Python editor “Idle” and open a Python shell
    Type
        import naoqi
    If you get no error messages Python and Naoqi are installed correctly
    You can use pip (Python Package Installer) to install packages
      In Windows: run cmd
      Type python –m pip install

## Slide 26: WinPython Installation (Easier!)
Install WinPython (see handouts)
  Includes most important extensions/libraries
Register WinPython using the WinPython Control panel
Install the Naoqi SDK for Python
Open the Python editor “Idle”
open a Python shell and type import naoqi
If you get no error messages Python is installed correctly

## Slide 27: Troubleshooting
    Make sure Python and Naoqi are installed in the right location
    Check the Python Path, add the location of Python and Naoqi to the python path
    Is Python 2.7 the only installation of Python?

## Slide 28: Installation
    Install numpy
    Install scipy
    OpenCV (if you need computer vision)
    Other useful libraries
      Tk (Universal window manager)
      PIL (Python Image Library)
      Matplotlib

## Slide 29: OpenCV
OpenCV is a huge library
You can try to find an installer for windows (previous slides)
Or, you download it form opencv.org
  Download and extract the files
  Copy the cv2.pyd file to your Python distribution
    I am using a 32bit machine with python 2.7
    Look for the file <path_to_opencv>\build\Python\x86\cv2.pyd
    Copy it to <path_to_python>\Lib\site-packages\cv2.pyd

## Slide 30: OpenCV
Test your installation using
  import cv2
We often use cv rather than cv2:
  import cv2.cv as cv
To automatically do this, create a file cv.py in to <path_to_python>\Lib\site-packages\ with the following content:
  from cv2.cv import *
This will enable the old “import cv” command

## Slide 31: NAO-lib
    A custom-built library simplifies many functions of Naoqi
    Meant for NAO, and the naoqi-version of NAO
    Latest version will be shared with you
      nao.py includes cv
      nao_nocv.py does not
    Installing nao-lib
      Create a directory with a python file with one line of code
        import nao_nocv as nao
      Copy nao.py or nao_nocv.py in the same directory
      Press F5 to run and test the program

## Slide 32: Simulated robot
    Installing the simulated robot
      Run the program naoqi-bin.exe that is installed along with Choregraphe
      Note your local IP address or use “127.0.0.1”
    Add the line
      Nao.InitProxy(“127.0.0.1”, [0])
    If all goes well you are connected to the simulated robot
      You can use Python to move the virtual robot in Choregraphe

## Slide 33: Simulated robot
Choregraphe
Run the program naoqi-bin.exe that is resides in the “bin” subdirectory of your choregraphe installation
Note your local IP address or use “127.0.0.1”
in your program add the line:
nao.InitProxy(“127.0.0.1”, [0])
If all goes well you are connected to the simulated robot

## Slide 34: Simulated robot
Webots
Run the webots program
Download the naoqisim project from canvas/…
Accept acces to private and domain networks
Open sample world “nao_indoors.wbt” from downloaded project location
Note your local IP address or use “127.0.0.1”
in your program add the line:
nao.InitProxy(“127.0.0.1”, [0])
If all goes well you are connected to the simulated robot

## Slide 35: Real robot
Connect the router
Start the robot by pressing the chest button
Press once on the chest button to hear Nao say its own ip address. If it cannot connect make sure the wireless configuration is ok (ask help)
Note the robot’s IP address e.g. “192.168.0.115”
in your program add the line
    nao.InitProxy(“192.168.0.115”, [0])
If all goes well you are connected to the real robot

## Slide 36: Real robot
General tips
To shut down the robot, press the chest button for 5 seconds
Testing
Test using the simulator! Just change the IP
If something goes wrong, press the chest button twice to release the joint stiffness (do this quickly like a double click)
Always pick it up by the waist
Always place the robot on the floor during testing
Put soft foam behind the robot

## Slide 37: Simple commands
    nao.Say(“Hello”)
    nao.InitPose() #the robot stands up and its joints stiffen
    nao.Crouch() #the robot sits down and releases its joint stiffness
    Always start with InitPose and end with Crouch
      It will stiffen and release the joints
      It provides a standard posture
      It prevents “overheating” if the crouches when doing nothing