## Slide 1: Using nao.py
Its main purpose is to create all the proxies you need
naoqi nao.py
global audioProxy
global motionProxy
global memoryProxy
global cameraProxy
global faceProxy
global ledProxy
global tts
global trackfaceProxy
global playProxy
global videoProxy
global asr
global speechProxy # same as asr
global sonarProxy
global postureProxy
"ALAudioDevice”
"ALMotion”
"ALMemory”
"ALVideoDevice”
"ALFaceDetection”
"ALLeds”
"ALTextToSpeech”
"ALFaceTracker”
"ALAudioPlayer”
"ALVisionToolbox”
"ALSpeechRecognition”
"ALSonar”
"ALRobotPosture"

## Slide 2: Using nao.py
You can use functions from naoqi directly once the proxies have been initialized:
Or you use a shorthand from nao.py (if available)
import nao_nocv as nao
nao.InitProxy(robot_IP)
nao.motionProxy.setTargetWalkVelocity(1.0,0.0.0.0.1.0)
nao.move(1.0,0.0.0.0.1.0)

## Slide 3: Using nao.py
The sonar needs to be initialized before it can be used
After that the left and right sonar values can be read. It returns the distance in m.
Turn it off using:
nao.InitSonar(True)
[SL, SR]=nao.ReadSonar()
nao.InitSonar(False)

## Slide 4: Using nao.py
The videocamera needs to be initialized before it can be used
To retrieve an image use
nao.InitVideo(resolution)
#resolution is 0, 1, 2, 3 corresponding to
#[160,120],[320,240],[640,480],[1280,960]
Image=nao.GetImage()

## Slide 5: Using nao.py
Facetracking can be enabled/disabled with:
To detect a face use
Search for a face using
nao.ALTrack(True) # turn on motors and enable face tracking
nao.ALTrack(False) #disable face tracking
nao.EndTrack() #turn motors off
nao.InitTrack() # turn motors on again
[face_x, face_y], detected = nao.ALFacePosition()
nao.FindFace()
# optional arguments (gain=1.0, offset=[0.0, -0.2])

## Slide 6: Using nao.py
There are two default postures:
Note: Prior to version 1.40 InitPose expects a crouch pose!!
From version 1.40
nao.InitPose() # stand up and turn motors on
nao.Crouch() # goto crouch pose and turn motors off
nao.GoToPosture(the_pose)
#Available postures are “Stand”, “Sit”, “Crouch”, …

## Slide 7: Using nao.py
For walking there are two variants.
The first variant sets the heading direction and speed (don’t forget to turn it off! (zero speed)):
The second method expects a distance in m.
Turn motors on with
nao.Move(dx, dy, dtheta, freq)
""""
dx = forward speed, dtheta = rotational speed,
dy = sidewards speed, freq = step frequency.
Allows Nao to move in a certain direction
with a certain speed.
All values should be -1 and 1 except freq between 0 and 1
"""
nao.Walk(dx, dy, dtheta)
nao.InitPose() # stand up and turn motors on
nao.Stiffen() # turns all motors on

## Slide 8: Using nao.py
For moving the head
Don’t forget to turn the headmotors on/off
nao.MoveHead(yaw_val=0, pitch_val=0, isAbsolute=True, timeLists=[[1],[1]])
yaw=nao.GetYaw():
pitch = nao.GetPitch():
yaw, pitch = nao.GetYawPitch():
nao.InitTrack()
nao.EndTrack()