## Slide 1: Manual nao-lib

## Slide 2: Using nao.py
Before you can use nao.py you need to import it and initialize it
nao.InitProxy connects to the robot specified by the IP address of the robot.
import nao_nocv_2_0 as nao
robot_IP=“127.0.0.1”
nao.InitProxy(robot_IP)

## Slide 3: Using nao.py
You can also specify which proxies (default [0]) and which port number (default 9559)
import nao_nocv_2_0 as nao
robot_IP=“192.168.0.115”
robot_PORT=52030
proxy_list=[1 2 3]
nao.InitProxy(robot_IP, proxy_list, robot_PORT)

## Slide 4
proxy_list naoqi nao.py
global audioProxy
global motionProxy
global memoryProxy
global cameraProxy
global faceProxy
global ledProxy
global tts
global trackfaceProxy
global playProxy
global videoProxy
global asr
global speechProxy # same as asr
global sonarProxy
global postureProxy
global landmarkProxy
global soundProxy
global soundLocalizationProxy
global trackerProxy
"ALAudioDevice”
"ALMotion”
"ALMemory”
"ALVideoDevice”
"ALFaceDetection”
"ALLeds”
"ALTextToSpeech”
"ALFaceTracker”
"ALAudioPlayer”
"ALVideoRecorder”
"ALSpeechRecognition”
"ALSonar”
"ALRobotPosture”
"ALLandMarkDetection"
"ALSoundDetection”
"ALAudioSourceLocalization”
"ALTracker"
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17

## Slide 5: Using nao.py
You can use functions from naoqi directly once the proxies have been initialized:
Or you use a shorthand from nao.py (if available)
The numbers are the normalized forward velocity, side-step velocity and turn-rate
import nao_nocv_2_0 as nao
robot_IP=“127.0.0.1”
nao.InitProxy(robot_IP)
nao.motionProxy.moveToward(1.0, 0.0, 0.0)
Nao.Move(1.0, 0.0, 0.0)

## Slide 6: Using nao.py
The sonar needs to be initialized before it can be used
After that the left and right sonar values can be read. It returns the distance in m.
Turn it off using:
nao.InitSonar(True)
[SL, SR]=nao.ReadSonar()
nao.InitSonar(False)

## Slide 7: Using nao.py
The videocamera needs to be initialized before it can be used
To retrieve an image use (with openCV only)
nao.InitVideo(resolution)
#resolution is 0, 1, 2, 3 corresponding to
#[160,120],[320,240],[640,480],[1280,960]
Image=nao.GetImage()

## Slide 8: Using nao.py
Facetracking can be enabled/disabled with:
To detect a face use
Search for a face using
nao.ALTrack(True) # turn on motors and enable face tracking
nao.ALTrack(False) #disable face tracking
nao.EndTrack() #turn head motors off
nao.InitTrack() # turn head motors on again
detected, timestamp, [face_x, face_y] = nao.DetectFace()
nao.FindFace()
# optional arguments (gain=1.0, offset=[0.0, -0.2])

## Slide 9: Using nao.py
LandMark detection needs to be initialized before it can be used
After that the Landmark can be detected using:
MarkerInfo is an array of detected landmarks
Each detected landmark contains 6 fields, for example the first detected landmark contains:
nao.InitLandMark()
detected, timestamp, markerInfo=nao.DetectLandMark()
markerinfo[0][0] #markerID
markerinfo[0][1] #alpha - x location in camera angle
markerinfo[0][2] #beta - y location
markerinfo[0][3] #sizeX
markerinfo[0][4] #sizeY
markerinfo[0][5] #orientation about vertical w.r. Nao's head

## Slide 10: Using nao.py
Sound detection needs to be initialized before it can be used
After that Sound can be detected using:
Marker Info is an array with the following fields:
nao.InitSoundDetection()
detected, timestamp, soundInfo=nao.DetectSound()
soundInfo[0] #index of sound start/end
soundInfo[1] #type: 1=start, 0=end
soundInfo[2] #confidence: probability that there was a sound

## Slide 11: Using nao.py
Sound Localization needs to be initialized before it can be used
After that Sound can be detected using:
Marker Info is an array with the following fields:
nao.InitSoundLocalization(switch=True)
detected, timestamp, soundInfo=nao.DetectSoundLocation()
soundInfo[0] #azimuth angle
soundInfo[1] #elevation angle
soundInfo[2] #confidence: probability that there was a sound
soundInfo[3] #Headposition 6D

## Slide 12: Using nao.py
There are two default postures:
Note: Prior to version 1.40 InitPose expects a crouch pose!!
From version 1.40
nao.InitPose() # stand up and turn motors on
nao.Crouch() # goto crouch pose and turn motors off
nao.GoToPosture(the_pose)
#Available postures are “Stand”, “Sit”, “Crouch”, …

## Slide 13: Using nao.py
For walking there are two variants.
The first variant sets the heading direction and speed (don’t forget to turn it off! (zero speed)):
The second method expects a distance in m.
Turn motors on with
nao.Move(dx, dy, dtheta, freq)
""""
dx = forward speed, dtheta = rotational speed,
dy = sidewards speed, freq = step frequency.
Allows Nao to move in a certain direction
with a certain speed.
All values should be -1 and 1 except freq between 0 and 1
"""
nao.Walk(dx, dy, dtheta)
nao.InitPose() # stand up and turn motors on
nao.Stiffen() # turns all motors on

## Slide 14: Using nao.py
For moving the head
Don’t forget to turn the headmotors on/off
nao.MoveHead(yaw_val=0, pitch_val=0, isAbsolute=True, timeLists=[[1],[1]])
yaw=nao.GetYaw():
pitch = nao.GetPitch():
yaw, pitch = nao.GetYawPitch():
nao.InitTrack()
nao.EndTrack()

## Slide 15: Speech recognition
Speech recognition first needs to be initialized with the words to be recognized
Once initialized, speech recognition needs to be turned on.
When speech recognition is on, you can detect speech using:
myWordList=[“Hello”, “Yes”, “No”, What is your name?”]
mylanguage=“English”
nao.InitSpeech(myWordlist,myLanguage)
nao.asr.subscribe(“MyModule”)
result=nao.DetectSpeech()

## Slide 16: Speech recognition
The result contains the list of recognized words and the probability of being correct. The list is sorted, so that the most probable word is always first in the list
If the robot needs to speak again you first need to turn speech recognition off.
The next slide shows a simple demo
result=[“MyFirstWord”, 0.312414, “MySecondWord”, 0.103141]
result=nao.asr.unsubscribe(“MyModule”)

## Slide 17: Speech recognition
def testspeech(maxcount=50):
wordList=["yes","no","hello", "Nao","goodbye"]
the_language="English"
nao.InitSpeech(wordList,the_language)
count=0
nao.asr.subscribe("MyModule")
while count<maxcount:
result=nao.DetectSpeech()
if len(result)>0:
print result
nao.asr.unsubscribe("MyModule")
nao.Say("You said: "+result[0]+".")
time.sleep(0.2)
nao.asr.subscribe("MyModule")
time.sleep(0.2)
count=count+1
nao.asr.unsubscribe("MyModule")

## Slide 18: Run movements
Using choregraphe, one can export movement files to Python
To run them, make sure that these movement files are findable by Python in a gestures subdirectory.
Typically you put all “gestures” in a subdirectory “gestures” of your project. The file extension is by default “.py” or “.ges”
To list all available gestures:
To play back single gesture:
nao.GetAvailableGestures()
nao.RunMovement(“the_name_of_the_gesture.py”)

## Slide 19: Run LED patterns
To run LED patterns, make sure that these LED pattern files are findable by Python in a “led” subdirectory.
Typically you put all LED patterns in a subdirectory “led” of your project.
To list all available LED patterns:
To play back single LED pattern:
nao.GetAvailableLEDPatterns()
nao.RunLED(“the_name_of_the_led_pattern.led”)

## Slide 20: LED Pattern files
A LED pattern is a csv file (“;” as delimiter)
The first row contains text labels
Groupname specifies the LED group as defined in naoqi (see SDK manual)
r,g,b are integers between 0 and 255 that specify the RGB colour
Frequency is the frequency in Hz; 0 is continuously on
Duration specifies the duration of the colour in s.
groupname(see help.txt) | r | g | b | frequency(0 = continuously on) | duration
FaceLeds | 0 | 20 | 80 | 0 | 0.5
FaceLeds | 0 | 0 | 0 | 0 | 2

## Slide 21: LED Pattern files
Available groups:
['AllLeds', 'AllLedsBlue', 'AllLedsGreen', 'AllLedsRed', 'BrainLeds', 'BrainLedsBack', 'BrainLedsFront', 'BrainLedsLeft', 'BrainLedsMiddle', 'BrainLedsRight', 'ChestLeds', 'EarLeds', 'FaceLed0', 'FaceLed1', 'FaceLed2', 'FaceLed3', 'FaceLed4', 'FaceLed5', 'FaceLed6', 'FaceLed7', 'FaceLedLeft0', 'FaceLedLeft1', 'FaceLedLeft2', 'FaceLedLeft3', 'FaceLedLeft4', 'FaceLedLeft5', 'FaceLedLeft6', 'FaceLedLeft7', 'FaceLedRight0', 'FaceLedRight1', 'FaceLedRight2', 'FaceLedRight3', 'FaceLedRight4', 'FaceLedRight5', 'FaceLedRight6', 'FaceLedRight7', 'FaceLeds', 'FaceLedsBottom', 'FaceLedsExternal', 'FaceLedsInternal', 'FaceLedsLeftBottom', 'FaceLedsLeftExternal', 'FaceLedsLeftInternal', 'FaceLedsLeftTop', 'FaceLedsRightBottom', 'FaceLedsRightExternal', 'FaceLedsRightInternal', 'FaceLedsRightTop', 'FaceLedsTop', 'FeetLeds', 'LeftEarLeds', 'LeftEarLedsBack', 'LeftEarLedsEven', 'LeftEarLedsFront', 'LeftEarLedsOdd', 'LeftFaceLeds', 'LeftFaceLedsBlue', 'LeftFaceLedsGreen', 'LeftFaceLedsRed', 'LeftFootLeds', 'RightEarLeds', 'RightEarLedsBack', 'RightEarLedsEven', 'RightEarLedsFront', 'RightEarLedsOdd', 'RightFaceLeds', 'RightFaceLedsBlue', 'RightFaceLedsGreen', 'RightFaceLedsRed', 'RightFootLeds']

## Slide 22
A simple test:
def testleds():
leds=nao.GetAvailableLEDPatterns()
for l in leds:
print "LED pattern ", l,
nao.RunLED(l)
time.sleep(3)
print " done."

## Slide 23: NaO-Lib REference

## Slide 24
nao.InitProxy(robot_IP, proxy_list , robot_PORT)
Connects to the robot specified by IP address and port number (default 9559)
Defines globals of the proxies specified in proxy_list
proxy_list is a list of integers. If the list contains 0, it will try to connect all proxies (default [0] ).
def InitProxy(IP="marvin.local", proxy=[0], PORT = 9559):
"""proxy: (list) 1->TTS, 2->audio, 3->motion,
4->memory, 5->face, 6->video,
7->LED's, 8->Track, 9->Speech,
10->Audioplayer, 11->VisionRecorder, 12->sonar,
13->posture, 14->landmark, 15->sounddetection,
16->soundlocalization, 17->tracker"""

## Slide 25
proxy_list naoqi nao.py
global audioProxy
global motionProxy
global memoryProxy
global cameraProxy
global faceProxy
global ledProxy
global tts
global trackfaceProxy
global playProxy
global videoProxy
global asr
global speechProxy # same as asr
global sonarProxy
global postureProxy
global landmarkProxy
global soundProxy
global soundLocalizationProxy
global trackerProxy
"ALAudioDevice”
"ALMotion”
"ALMemory”
"ALVideoDevice”
"ALFaceDetection”
"ALLeds”
"ALTextToSpeech”
"ALFaceTracker”
"ALAudioPlayer”
"ALVideoRecorder”
"ALSpeechRecognition”
"ALSonar”
"ALRobotPosture”
"ALLandMarkDetection"
"ALSoundDetection”
"ALAudioSourceLocalization”
"ALTracker"
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17

## Slide 26
nao.Move(dx,dy,dtheta)
Non-blocking call that sets the robot in motion.
  dx, dy are the normalized forward and side-step velocity (in SI: dx*0.04 m/s)
  dtheta is the normalized turn-rate (in SI: dx*0.349 rad/s)
  Freq is the normalized step-frequency (not used in naoqi 2.1.x)
def Move(dx=0, dy=0, dtheta=0, freq=1):
""""
dx = forward speed, dtheta = rotational speed,
dy = sidewards speed, freq = step frequency.
Allows Nao to move in a certain direction
with a certain speed.
"""